## Slide 1
AIoT-Based Smart Climate-Aware Greenhouse System for Sustainable Agriculture
Muhammad Maaz
Muhammad Talha Khan
Muhammad Ibad Khan
Department of Computer Systems Engineering
University of Engineering & Technology Peshawar

## Slide 2
The Problem: The Inconsistency of Traditional Agriculture
Inconsistency and Delay: Traditional plant care suffers from inconsistency and delayed intervention, often leading to crop loss or suboptimal yields.
Lack of Precision: Environmental factors require constant, precise management that is difficult to achieve manually.
Reactive Intervention: Disease detection is often reactive, occurring only after visible symptoms have caused significant damage, limiting medicinal or high-value crop viability.
Resource Inefficiency: Irrigation and climate control are often managed inefficiently, wasting water and energy.

## Slide 3
OBJECTIVES
Platform Development: Build a robust Internet of Things (IoT) hardware platform for real-time environmental sensing and automated device control (pumps, fans).
Intelligent Control: Train a Machine Learning (ML) model to intelligently dictate automated control actions based on sensed data.
Early Disease Detection: Implement real-time leaf image classification for early detection and alerting of plant diseases.
Global Adaptability: Develop a system capable of storing seasonal data and using it to configure optimal growing parameters for medicinal and specialty plants in diverse global regions.
User Interface: Provide a comprehensive, cross-platform mobile application and web dashboard for remote monitoring, analysis, and control.

## Slide 4
Literature Review / Background
Project Focus: AIoT-Based Smart Climate-Aware Greenhouse System for Sustainable Agriculture.
Technology Stack: The project utilizes the Artificial Intelligence of Things (AIoT) framework, combining IoT sensing with Edge AI processing.
Core Principle: Addressing the need for precise environmental control through automation and data-driven decision-making.
System Foundation: Building an IoT hardware platform for sensing and control.
Scalability: Designed to be easily expanded to multiple greenhouses with a single central hub (Raspberry Pi).

## Slide 5
Methodology: Automated Sensing and Intelligent Actuation
Sensing: Uses a soil moisture sensor to check moisture level and a DHT22 for temperature and humidity.
Irrigation Control: When soil moisture drops, the motor turns on and activates the irrigation system.
Climate Control: When temperature gets high, the servo motor and fan turn on. The fan speed adjusts automatically.
Communication: NRF modules are used for wireless data transmission between the node and the Raspberry Pi.
Intelligent Control: An ML model dictates the control actions (pump, fan, ventilation) intelligently.

## Slide 6
Automation System

## Slide 7
System Architecture: Edge AI Gateway and Multi-Node Scalability
Sensor Node: Microcontroller collects sensor data (Moisture, Temp/Humidity) and controls actuators (Pump, Fan).
Wireless Link: NRF Transceiver sends data wirelessly.
Edge AI Gateway: Raspberry Pi receives data from NRF nodes and executes the optimized ML model.
Cloud Interface: Firebase Dashboard provides real-time monitoring and logging.
User Interface: Flutter mobile app enables remote control and data visualization.

## Slide 8
Technologies & Tools Used
Component/Phase | Technology/Tool | Role in System
Edge Hardware | Raspberry Pi | The resource-constrained host, performing all processing on-device (Edge AI).
Model Runtime | TensorFlow Lite (tflite_runtime) | Lightweight core library for executing the optimized ML model on the Pi's ARM CPU.
Data & Cloud | Firebase Studio | Real-time, cloud-based monitoring interface.
Video Processing | OpenCV (cv2) | Handles real-time camera stream and pre-processing (e.g., resizing to 224×224 pixels).
User Interface | Flutter | Used to build a modern, intuitive, cross-platform interface (Android/iOS).
Communication | NRF Modules | Enables wireless data transfer and scalability to multiple greenhouses.

## Slide 9
ML Data: Control and Image Pre-processing
Control Data:
Description: Sensor readings (Moisture, Temp, Humidity) mapped to actuator states (Pump ON/OFF, Fan ON/OFF, Ventilation ON/OFF).
Goal: Train a classification model for intelligent decision-making.
Image Data (for Disease Detection):
Description: Images of plant leaves for health classification.
Preprocessing: The real-time camera stream is handled by OpenCV. Captured frames are resized to 224 times 224 pixels before being fed to the TensorFlow Lite model.
Training Outcome: The model was trained successfully with accuracy stabilizing around 74% and loss minimizing very quickly

## Slide 10
Machine Learning for Control and Detection
Model Type: Classification model for control actions and image classification for health monitoring.
Control Logic: The model determines the optimal ON/OFF state for the Pump, Fan, and Ventilation based on sensor data.
Deployment: Model is optimized and executed on the resource-constrained Raspberry Pi using TensorFlow Lite (Edge AI).
Reliability: The model demonstrated high reliability in control, with validation metrics closely mirroring training metrics (no catastrophic overfitting).

## Slide 11
Core Features: Automation, Edge AI, and Remote Management
Intelligent Automation: ML-dictated control of irrigation (Pump) and climate (Fan/Ventilation).
Real-Time Dashboard (Firebase): Cloud-based monitoring showing live KPIs and a Leaf Health Index.
Early Disease Detection (Edge AI): Real-time image classification on the Raspberry Pi identifies plant health issues.
Mobile App: Cross-platform access for remote management, data visualization, and early alarming.
Scalability: System can be expanded to manage multiple NRF nodes across multiple greenhouses.

## Slide 12
Firebase Dashboard

## Slide 13
App Dashboard
User Interface (UI)
Cross-Platform Interface (Flutter):
1) The system uses Flutter to build a modern, intuitive Smart Greenhouse application. This allows the same codebase to run on both Android and iOS, providing wide accessibility for monitoring.
2) Real-Time Data Visualization: The mobile app displays key sensor metrics in real-time, including Temperature, Humidity, Soil Moisture, and Fan Speed. This gives the user immediate visibility into the greenhouse environment.
3) Remote Control and Automation: The application includes toggle controls (switches) for activating components like the Pump and setting the system to Auto Mode (Automatic Control), allowing users to remotely manage the greenhouse conditions.

## Slide 14
Prototype Output: Live Dashboard and Mobile Interface
Dashboard Display:
Shows current conditions:
  Temperature: 24.7∘C
  Humidity: 67.4%
  Soil Moisture: 56.1%
Mobile App Interface:
Displays sensor metrics:
  Temperature: 29.5∘C
  Fan Speed: 70%
Provides toggles for:
  Pump
  Auto Mode
Terminal Output (Raspberry Pi):
Shows system processes and package installations:
  OpenCV
  Debian Trixie

## Slide 15
System Deployment and Validation
Hardware Implementation: Successfully implemented the IoT hardware platform, integrating sensors, actuators, and NRF wireless communication.
Model Training and Deployment: Trained the ML model and deployed it on the Raspberry Pi using TensorFlow Lite for intelligent control actions.
System Reliability: Achieved a model accuracy of 74.6%, with control decisions demonstrating extremely high reliability (AUC = 1.00) on the test set.
User Interface: Developed a functional Firebase dashboard and a cross-platform Flutter mobile application for real-time monitoring and remote control.

## Slide 16
Accuracy

## Slide 17
Results & Evaluation
Overall Test Accuracy: 74.6%.
Control System Accuracy: The ML model achieved extremely high accuracy and low error rates for all three control systems (Pump, Fan, Ventilation).
ROC Curve (AUC): 1.00 for Pump, Fan, and Ventilation.
Precision-Recall: Average Precision = 1.00 for Pump, Fan, and Ventilation.
Conclusion: These scores indicate the model is making the correct control decisions (ON/OFF) based on sensor data with virtually perfect accuracy on the test set.

## Slide 18
ROC Curve and Precision-Recall curve

## Slide 19
Key Challenges in AIoT Deployment
Hardware Implementation: Successfully implemented the IoT hardware platform, integrating sensors, actuators, and NRF wireless communication.Hardware Integration: Integrating diverse components (Arduino/microcontroller, Raspberry Pi, NRF modules, relays, sensors) into a cohesive, reliable system.
Model Optimization for Edge: Optimizing the machine learning model (e.g., for image classification) to run efficiently on the resource-constrained Raspberry Pi CPU using TensorFlow Lite.
Data Reliability: Ensuring the consistency and integrity of sensor data transmitted wirelessly via NRF modules.
Scalability Management: Configuring a single Raspberry Pi to efficiently manage data and commands from multiple NRF nodes/greenhouses.
Model Training and Deployment: Trained the ML model and deployed it on the Raspberry Pi using TensorFlow Lite for intelligent control actions.
System Reliability: Achieved a model accuracy of 74.6%, with control decisions demonstrating extremely high reliability (AUC = 1.00) on the test set.
User Interface: Developed a functional Firebase dashboard and a cross-platform Flutter mobile application for real-time monitoring and remote control.

## Slide 20
Expanding to Global and Predictive Agriculture
Seasonal Data Repository: Implement storage and analysis of seasonal data to establish and optimize growth "recipes" for specific medicinal plants.
Global Adaptability: Develop logic to use stored seasonal data to automatically adjust greenhouse parameters based on a region's current climate, enabling global crop viability.
Predictive Maintenance: Incorporate advanced time-series analysis to predict component failures or required environmental adjustments.
Enhanced Sensing: Add support for more advanced sensors (e.g., pH, CO_2 concentration) for holistic crop management.

## Slide 21
Project Phases and Progress (Estimated Timeline)

## Slide 22
Conclusion: AIoT for Sustainable Precision Agriculture
System Success: We successfully developed and validated an AIoT-Based Smart Climate-Aware Greenhouse System.
Precision Control: The system delivers consistent, precise environmental management using a highly reliable ML control model (AUC= 1.00).
Key Features: Integrated with scalable wireless communication, a real-time monitoring dashboard, and a cross-platform mobile app for remote management and alarming.
Impact: This platform enables the sustainable and efficient cultivation of high-value and medicinal plants by mitigating environmental inconsistency and facilitating global crop viability.

## Slide 23
Thank You